## Slide 1: Neighbor Mgmt Policy
Performance Report
- Rahul, Rabi, Simon, Joakim
IETF104, Prague

## Slide 2: Updates
Text to highlight use of min-priority field in neighbor mgmt
  Referenced Michael’s enrollment draft
  draft-richardson-6tisch-roll-enrollment-priority
Clarifications on route cleanup and impact on neighbor cache
Performance result added

## Slide 3: Performance test config
Network stack
  LWIP integrated with RPL
  LWIP added with neighbor mgmt policy module
Test tool
  Whitefield-framework
    With NS3 backend for wireless simulation
    64 nodes network, 8x8 grid, 80x80 sq. mtr
    802.15.4 in 2.4GHz, Unslotted CSMA with single channel
  Data transmission
    UDP data sent by each node at 10s interval to BR
    BR echoes the packet

## Slide 4: What to measure?
Packet Delivery Rate
  How does neighbor management policy impact PDR?
Network convergence time
  How to define network convergence time in this context?

## Slide 5: Results
PDR
  >95% PDR achieved even with extremely constrained nbr-table
Network convergence time
Nbr cache size | Without NBR-mgmt | With NBR-mgmt
10 | No-convergence | 94sec
20 | No-convergence | 51sec
40 | 24sec | 25sec

## Slide 6: Observations
RPL Control overhead with neighbor management was high
  Because of proactive maintenance
  Convergence time and control overhead is high with lower nbr cache size
Without neighbor management
  The BR could get all the routes but neighbor table size was not enough
  Most of the UDP traffic was dropped at BR or en-route because of next-hop unavailability in neighbor table

## Slide 7: Next?
We believe the document is ready for LC